## Slide 1: Hot-Wiring of the Future: Exploring Car CAN Buses
ENGS 89/90: Final Presentation
Chris Hoder
Ted Sumers
Grayson Zulauf
7 March 2013
Sponsored by:
Notes: Cover Page

## Slide 2: Background
Automobiles as complex, highly-connected networks
engineering.dartmouth.edu 7 March 2013

## Slide 3: Problem Statement
Problem:
Safety-critical information is transmitted on an unauthenticated network. Adversaries could exploit this with unknown consequences.
Need:
A better understanding of the scope of the problem and tools to further explore the space.
engineering.dartmouth.edu 7 March 2013

## Slide 4: State of the Art
Inexpensive (<$200)
Handheld, Basic Diagnostics
Simple debugging
Midrange ($200-500)
Link to computer
More sophisticated analysis (horsepower, torque, mileage)
Advanced (>$2500, licensed by manufacturer)
In-depth analysis
Writing capabilities
  Re-flash ECU firmware
CAN Protocol Analyzers
engineering.dartmouth.edu 7 March 2013

## Slide 5: State of the Art – Academic Research
To carry out an attack, an adversary must have all of the following:
Incentive
Toehold
Identified Exploits
engineering.dartmouth.edu 7 March 2013

## Slide 6: State of the Art – Academic Research
To carry out an attack, an adversary must have all of the following:
Incentive
Toehold
Identified Exploits
Identified
OBD-II Port
Project Scope
engineering.dartmouth.edu 7 March 2013

## Slide 7
Explore potential market for automotive security products.
engineering.dartmouth.edu 7 March 2013

## Slide 8
Explore potential market for automotive security products.
Prove Vulnerability
Further Research
engineering.dartmouth.edu 7 March 2013

## Slide 9
Explore potential market for automotive security products.
Prove Vulnerability
Further Research
Proof-of-Concept:
Demo Hack
Methodology
Software Package
engineering.dartmouth.edu 7 March 2013

## Slide 10: Software Package: Goals
GoodThopter10
CAN Bus
Software Package
User
engineering.dartmouth.edu 7 March 2013

## Slide 11
Read/Write Capability
User Interface
Data Management
Software Package
engineering.dartmouth.edu 7 March 2013

## Slide 12: Reverse-Engineering the CAN Bus
General Network Attack Methodology
Toehold
Passive Listening
Active Probing
Attack
Physical Stimuli
Identify Exploits
Incentive
engineering.dartmouth.edu 7 March 2013

## Slide 13: Work Accomplished - Methodology
Correlation with Physical Stimuli
Packet Injection
Background Characterization
engineering.dartmouth.edu 7 March 2013

## Slide 14: Work Accomplished - Methodology
Correlation with Physical Stimuli
Packet Injection
Arbitration ID Sweep
RTR Sweep
Unfiltered Sniff
Filtered Sniff
Background Characterization
engineering.dartmouth.edu 7 March 2013

## Slide 15: Work Accomplished - Methodology
ArbID | 512 | 513 | 529 | 530 | 560 | 1056 | 1057 | 1072 | 1248 | 1279
Freq (packets/second) | 115 | 62 | 50 | 50 | 112 | 10 | 0.2 | 50 | 1 | 1
Arbitration ID Sweep
RTR Sweep
Unfiltered Sniff
Filtered Sniff
engineering.dartmouth.edu 7 March 2013

## Slide 16: Work Accomplished - Methodology
Arbitration ID Sweep
RTR Sweep
Unfiltered Sniff
Filtered Sniff
ArbID | Frequency (packets/second) | Background Packets
513 | 62 | 12 xx 125 xx 39 16 0 125
*xx = varying
A Case Study – ID 513
engineering.dartmouth.edu 7 March 2013

## Slide 17: Work Accomplished - Methodology
Correlation with Physical Stimuli
Packet Injection
Background Characterization
engineering.dartmouth.edu 7 March 2013

## Slide 18: Work Accomplished - Methodology
Packet Injection
Background Characterization
Correlation with Stimuli
System Perturbation
Characterize Change with Stimuli
List of Perturbations
engineering.dartmouth.edu 7 March 2013

## Slide 19: Work Accomplished - Methodology
System Perturbation
Characterize Change with Stimuli
A Case Study – ID 513
ArbID | Perturbation Response | Data Byte Correlation
513 | Revving Engine | Bytes 0, 1
 | Increase while driving | Byte 4
engineering.dartmouth.edu 7 March 2013

## Slide 20: Work Accomplished - Methodology
Correlation with Physical Stimuli
Packet Injection
Background Characterization
engineering.dartmouth.edu 7 March 2013

## Slide 21: Work Accomplished - Methodology
Correlation with Physical Stimuli
Background Characterization
Confirm Inferences, Test Responsiveness
Boundary Analysis
Generative Fuzzing
Confirm New Inferences
Packet Injection

## Slide 22: Work Accomplished - Methodology
Confirm Inferences, Test Responsiveness
Boundary Analysis
Generative Fuzzing
Confirm New Inferences
ArbID | Fuzzing Response | Refined Inferences
513 | Dashboard components change | Bytes 0, 1 = RPM
 |  | Byte 4 = Speedometer
A Case Study – ID 513
engineering.dartmouth.edu 7 March 2013

## Slide 23: Higher Level Protocol: ID 513
Chart: Data Byte 4 Value
| 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0 | 110.0
 | 0 | 18 | 34 | 50 | 66 | 82 | 98 | 114
 | 60 | 61 | 45 | 30 | 15 | 0
engineering.dartmouth.edu 7 March 2013

## Slide 24: Higher Level Protocol: ID 1056
1056
DLC = 8
Engine Temp
Odometer
Battery Charge
Engine Clock
Dashboard Warnings
Check Fuel Cap
Unused
Counter
SOF
Arbitration ID
Control Field
Data Field
EOF
engineering.dartmouth.edu 7 March 2013

## Slide 25
Read/Write Capability
User Interface
Data Management
Software Package
engineering.dartmouth.edu 7 March 2013

## Slide 26: Video
engineering.dartmouth.edu 4 March 2013
Notes: This is the youtube video.

## Slide 27: User Interface: Design Considerations
engineering.dartmouth.edu 7 March 2013

## Slide 28
Raw CAN Data
Simple communications with Goodthopter10
Digital Logic communications
Generic Analysis Tools
Experimental Methods
Advanced communications
Custom Module
Car/User Specific
Not necessary
Custom Module
Generic Analysis Tools
Raw CAN Data
engineering.dartmouth.edu 7 March 2013

## Slide 29: Future Work
Hardware:
Optimize Siege’s firmware
Modern Test Vehicle:
Newer cars are more vulnerable
engineering.dartmouth.edu 7 March 2013

## Slide 30: Thank you
Project Sponsor:
Siege Technologies and Daniel Bilar
Advisors:
Sergey Bratus
Vincent Berk
Technical Consultants
Andrew Righter
Travis Goodspeed
Course Instructors
Professor Collier
Professor Lotko
The Review Board
engineering.dartmouth.edu 7 March 2013